## Slide 1: Scanbook project
Wesley Estievenart – Thomas Herpoel – Michael Manzella

## Slide 2: Introduction
Scanbook = Semi-automatic book scanner
2016
2017
Notes: Some of you may not know what is the Scanbook project. It’s a semi-automatic book scanner and it’s purpose is to facilitate the process of digitizing a book by automatizing as much part of the process as possible. Allow me to start with the results for once. On the left part of the slide you can see last year’s system and the right picture is the new one. Obviously you can spot a lot of changes between the two ! Basically every part of the design has changed: the mechanical system, the electronic and the software.

## Slide 3: Introduction
Old system’s flaws
Controlled by Computer
Lack of stability
New system’s goals
Controlled by embedded electronic
…
Notes: We come from the old system which had a lot of flaws. The left picture is the last year system and the right picture is the new one. There are a lot of changes between the two ! The changes are in the mechanical, the electronic and the software part.

## Slide 4: Introduction System design overview
Notes: This is the global schematic of the Scanbook. The main component is the Raspberry Pi 3 which replaces the computer to control the whole system. The Raspberry Pi interacts with the two cameras and the motor control PCB. Cameras are connected to the Raspberry Pi through a switch circuit (because there is only one camera port on the Raspberry Pi). The PCB controls the motor and this one controls the mechanical part. The mechanical part is composed by Plexiglas windows and the two sensor mechanism to detect when the windows are at the UP or DOWN position.

## Slide 5: Content
Development
Results
Encountered issues
Conclusion

## Slide 6: Development
Mechanics
Electronics
Software
  Image processing
  Control

## Slide 7: Development : Mechanics
CAD
+
3D printing

## Slide 8: Development : Mechanics

## Slide 9: Development : Mechanics Modular design
Easy to 3D print base part
Complex module
3D printed small module
Interconnects “off the shelf” parts
  Regular M8 threaded rods
Make big 3D structure possible!

## Slide 10: Development : Mechanics Down position detection
Two-part system
  One fixed to the motorization’s belt
  One fixed to the glasses
One micro switch in between
When the glasses hit an obstacle (book)
  The micro switch triggers

## Slide 11: Development : Mechanics Many other parts…

## Slide 12: Development
Mechanics
Electronics
Software
  Image processing
  Control

## Slide 13: Development : Electronics Motor driver issue
When motor disabled :
Mobile part moves freely (thanks to gravity)
Back EMF generated in motor coils
Flyback diodes in the driver IC break down
Solution :
Force /ENABLE to GND
Motor is always enabled
AD4988 Driver IC
Notes: Epxliquer le probleme et la solution

## Slide 14: Development : Electronic
Two part
  Power supply
  Motor control
Modified to solve driver problem
  The motor driver is always powered and enabled
Reused PCB from Scanbook 2015-2016
  Modified to match the new circuit
Notes: The PCB used to control the motor is represented on the two pictures. It is composed by two main part : the power supply and the motor control part.
The power supply part has three switches to control all the voltages. And there is also a rectifier to convert the supply voltage (about 10-12 V) to a +5V voltage. The +5V voltage is used to supply the microcontroller and the driver for stepper motor. And the supply voltage is used to supply the stepper motor. The rectifier allows to have a single external power supply.
The motor control part has a microcontroller, a stepper motor driver and several connectors. The microcontroller exchange messages with the Raspberry PI and controls the stepper motor driver. This one control the stepper motor. Connectors are used to connect the Raspberry PI, the two sensors, the motor and the ISP (to program the microcontroller).
Last year’s PCB has been modified and reused because it works fine except from the motor driver problem.

## Slide 15: Development : Electronic Camera multiplexer
Image data transfer
Between Pi Camera and Raspberry Pi
High speed serial communication (up to 1 Gbps per lane)
Licensed protocol (expensive specifications under NDA)
Good news : a special purpose IC is available !
Bad news: it only exists in a really tiny QFN package …
MIPI DSI-4 lanes camera interface
Raspberry
Pi Camera

## Slide 16: Development : Electronic Camera multiplexer
Detection and configuration of the camera
Between Pi Camera and Raspberry Pi
Regular I²C communication
Good news : well known interface, easy to multiplex with regular logic IC
Bad news : actual configuration of the camera is hidden in a binary blob in the Raspberry Pi firmware (it is NOT open source)
CCI control interface
Raspberry
Pi Camera

## Slide 17: Development : Electronic Camera multiplexer
Fairchild’s FSA642 IC for MIPI DSI-4 lanes multiplexing
74CBTLV3257 MUX/DEMUX IC for I²C switching
Camera A is selected by default

## Slide 18: Development
Mechanics
Electronics
Software
  Image processing
  Control

## Slide 19: Development : Software Image processing
Notes: Concerning the image processing, we chose to use the OpenCV library on the Raspberry pi. It is a library specialized in real time image processing. After installing the library, we started to do several tests with the Pi Cameras used. Each of the cameras allow to take a single-page shot. These two cameras are connected to the electronic switch circuit seen previously.
The tests were carried out in two parts : the first step is to detect the outline of a page of the book and the second step is to correct and stretch the picture of a single page.
The following slides will present a simplified version of the image process steps.

## Slide 20: Development : Software Image processing
Original
Gray
Notes: At first, the color picture is converted to grayscales.

## Slide 21: Development : Software Image processing
Gaussian filter
Canny filter
Notes: Secondly, a Gaussian filter is applied to reduce the noise and the details of the picture. This step has the effect of blurring the picture.
Third, we apply a Canny filter which allows to detect the contours of all the elements in the picture.

## Slide 22: Development : Software Image processing
Contour detector
Rotation and stretching
Notes: Fourth, we apply a contour detection algorithm and display the retrieved contour on the colour picture.
And finally, we stretch the picture.

## Slide 23: Development
Mechanics
Electronics
Software
  Image processing
  Control

## Slide 24: Development : Software Control
Computer controlled => Raspberry PI 3 controlled
What is a Raspberry PI ?
O.S. installation, configuration
Programming & Image processing
Notes: As we said before, the system is now controlled by a Rasperry PI and not a computer. But what is a Raspberry PI ? It is a nano-computer that has the size of a credit card. Many models exist and the one used in the Scanbook project is the Rasperry Pi 3. It cost about € 35 and it allows to make the Scanbook a compact and autonomous system.
The control program of the Scanbook was developed on the Raspberry but it actually first required an O.S. and a lot of configuration to work properly !
The configurations concerned the image processing library, the serial communication with the PCB, the touch screen, and so on. Installation and all the configurations took time, about 16h !!!
After the installations and configurations were finished, the software development and image processing parts had finally started.

## Slide 25: Development : Software Control
Serial commands from Raspberry Pi to PCB :
  UP, DOWN, DISABLE, FULL, HALF, QUARTER, EIGHTH, SIXTEENTH
Serial commands from PCB to Raspberry Pi:
  ISUP, ISDOWN, ISSTOP, STEPSIZESET, ERROR
Ex . : UP command is received
  The stepper motor turn and when the UP sensor detects the Plexiglas windows, motor is automatically disable. Then, the PCB return ISUP command.
Notes: This is the list of commands exchanged from the Raspberry Pi to the PCB.
UP and DOWN commands are used to move the mobile part composed by the glasses. The DISABLE command is used to stop any movement. The five remaining commands are used to set the step size of stepper motor.
There are also commands sent by the PCB to the Raspberry Pi.
ISUP and ISDOWN commands are the answer to UP and DOWN commands. ISSTOP is the answer to DISABLE command and STEPSIZESET is the answer for the fives other commands.
There is also a ERROR command in case we need it later.
There is an example of command received from the Raspberry Pi. The PCB receives it and performs the command. The sensor detects the mobile part when it is in the top position, the PCB stop the movement and sends a ISUP command to the Raspberry Pi.

## Slide 26: Development : Software Control
Currently, controlled by 4 buttons on Raspberry Pi’s GPIOs:
  Start
  Next
  End
  Stop
Serial messages between Raspberry PI & PCB
UP and DOWN sensors connected on the PCB
Motor control on the PCB
Notes: The Scanbook is controlled by 4 buttons : Start, Next, End and Stop. The start button allows to start a new book, the next button is used to go to the next page, the end button is used to finish the book and the stop button allows to stop the scan and shut down the program. The Raspberry Pi sends and receives command and sensors information to control the mechanical part and the scan sequence.

## Slide 27: Development : Software Control
Initialisation
  Display « press start »
Start
  Up command
  Display « press next or end »
Next
  Down command
  Display « scan in progress »
  Takes pictures
  Image processing
  Return to start button process
End
  Display « scan completed »
  Return to initialisation process
Stop
  System shutdown
Notes: On the left, there are the actions performed when buttons are pressed in a complete scanning process.
First, the Scanbook is initialized and display “press start”. When the “start” button is pressed, the UP command is sent to the PCB and a new message is displayed “press next or end”. If the “next” button is pressed, DOWN command is sent, message is displayed, pictures are taken and processed, UP command is sent and a new message is displayed. If the “end” button is pressed, a message is displayed, the books is finished and the program return to the initialisation part. When the “stop” button is pressed, the system shutdown.
The diagram on the right shows the state machine of the system that defines this sequence.

## Slide 28: Content
Development
Results
Encountered issues
Conclusion

## Slide 29: Results : Mechanics

## Slide 30: Results : Electronic Camera multiplexer
2-layer PCB
Populated
FSA642 in QFN package : 2.5 x 3.4 mm

## Slide 31: Results : Electronic Camera multiplexer
Python
script

## Slide 32: Results : Image processing
Original
Gray + Gaussian filter
Notes: Here are the image processing results. The first tests performed were is to try to detect the outline of a whole book.
We have on the left the original picture and on the right the conversion into gray scale and with the Gaussian filter.

## Slide 33: Results : Image processing
Gray + Gaussian filter
Canny filter
Notes: Then we apply the Canny filter to detect the contour of the picture’s elements. We can see that with this algorithm we detect elements on the pages, like the figures.
A threshold value can be configured to tweak the detection.

## Slide 34: Results : Image processing
Canny filter
Contour detector
Notes: Finally, we apply the detection of contours and draw it. This test is successful, but let’s see what happens when the threshold value is changed.

## Slide 35: Results : Image processing
Threshold settings
Basic picture
Threshold Value
Notes: If we increase the threshold value, we see that some part of the inside of the pages, like parts of the text and the central part of the book, have disappeared.
In this case increasing the threshold is improving the result but we can also have the opposite effect by decreasing it.

## Slide 36: Results : Image processing
Threshold settings
Threshold Value
Threshold Value
Notes: If we lower the threshold value of the Canny filter, more elements of the book are appearing, like the figures and almost the whole text. The problem is that the result on the final detection of the contour will be worse and imperfections appear.

## Slide 37: Results : Image processing
Threshold settings
Notes: Here is the result of the contour detection algorithm with a lower threshold value. We can see a decrease in quality of the detected outline and also the detection of parasitic elements outside the book.

## Slide 38: Results : Image processing
Notes: Here are the two results with different threshold values. This first test allowed to illustrate the importance of the threshold value to obtain a satisfying result!

## Slide 39: Results : Image processing
Notes: The second test was performed to try the stretching and correction of the page. This test was done on a single-page picture.
After performing the steps mentioned previously to detect the contour, an algorithm detects the largest rectangle on the picture and return the coordinates of the four corners. We can see below the values of the four corners returned by the algorithm. The only remaining step is to stretch the image in the perfect shape.

## Slide 40: Results : Image processing
Notes: But we do not get a satisfying result. The problem is that a part of the second page is detected in the detection of our contour. The solution to this problem would be to hide this part in a software way by adding a black strip.

## Slide 41: Results : Image processing
Notes: In this example, we added a black strip to hide the second page. The result obtained is more satisfying than the previous one. But this solution can only be used if the cameras do not change position and depends on the size of the book

## Slide 42: Content
Development
Results
Encountered issues
Conclusion

## Slide 43: Encountered issues
Soldering a QFN component
  Really small component, requires hot air or oven soldering
Install the OpenCV library on Raspberry Pi
Serial communication configuration with a Raspberry Pi 3
  Serial interface is normally used with internal bluetooth component
Graphical interface configuration
43

## Slide 44: Content
Development
Results
Encountered issues
Conclusion

## Slide 45: Conclusion Current state of the project
Improved prototype
  3D printing allowed for a better mechanical system
Electronics
  Switch to connect two cameras
  Motor driver issue is solved
Image processing
  OpenCV in an embedded system

## Slide 46: Conclusion Perspectives
Mechanical improvements :
  3D parts conceptions
  Close the structure
Electronical improvements :
  Lighting system
  Add touch screen & graphical user interface
Software improvement :
  Implement PDF file generation
  Send the PDF file by mail
  Improve the image processing
  Use OCR ?

## Slide 47: Thank you for your attention !

## Slide 48: Questions